## Slide 1
Radiometer Physics GmbH
Meckenheim, Germany
Microwave, sub-mm, THz
Turn-key radiometers, space technology Components, design, scientific expertise

## Slide 2: Radiometer Physics GmbH
Founded 1973 by Dr. P. Zimmermann
40 (+) employees
Design / fabrication of MW-radiometers (mm, sub-mm)
Development of radiometer sub- systems (oscillators, mixers, waveguide components, planar networks, amplifiers, optics, etc.)
Active in the following fields:
Radio Astronomy
Plasma Physics
ESR Spectroscopy
Remote Sensing
Space borne radiometers
Network Analyzer Extensions

## Slide 3: RPG GmbH Organization
Rohde & Schwarz OEM RF Systems & Comp.
A. Walber, J. Oelrichs
Radiometer Systems
Dr. T. Rose, A. Mombauer,
Dr. H. Czekala
Space Projects
Dr. M. Brandt, Dr. M. Philipp R. Henneberger, Dr. H. Czekala
R&D Projects
R. Henneberger, Dr. M. Brandt, Dr. M. Philipp, Dr. B. Thomas
Business Divisions
FFTS Systems
R. Henneberger
Company Management
Managing Directors
Dr. T. Rose, A. Walber
Financials & Management Assistant
K. Ley
Managing Board
M. Lüders (R&S), Ch. Evers (R&S), Dr. T. Rose (RPG), A. Walber (RPG)
Sales & Marketing
Dr. H. Czekala, R. Henneberger
Business Development
Dr. H. Czekala, A. Walber, R. Henneberger, Dr. T. Rose
Operations & Activities
Design, Development & Analysis
Component and System Development
RF Component & Optics Simulations (CST, HFFS, ADS etc.)
Space Environment Simulation & Analysis
Meteorological Concepts & Retrievals
Scientific Consultancy
Software Development
Manufacture & Integration
Machine Shop
Electroforming Facilities
Clean Room MMIC Assembly
RF Component Manufacturing
R&S OEM Products Integration
Meteorological Radiometer Integration
Clean Room Space Product Integration
PA/QA, Test & Verification
Manufacturing Process Control
Semi-Automated ICD Verification
RF Performance Testing
RF Calibration
Antenna Pattern Measurements
R&S High-Rel BI & Thermal Cycle
Environmental Testing

## Slide 4: Fields of activity (2010)
Umsatz RPG: 5.300.000€
Chart: 
| Rohde&Schwarz | Radiometer | HF Komponenten & Systeme | Space | Förder- & Entwicklungsprojekte | Hornstrahler | FFTS Spectrometer
 | 37.5593 | 26.3188 | 20.5662 | 8.6059 | 1.7553 | 2.0049 | 3.1897
Meteorological
Remote Sensing
20% (+)

## Slide 5: Technology to Product
Knowledge, experience, precision and quality
Design
Development
Manufacture
Integration and Test
Electromagnetic
Simulation
Harmonic Balance
Electrical Solvers
Engineering
CAD  CNC
Machining +
Integration
Local Oscillator
Subsystem
FIRST/HIFI Instrument
on Herschel Satellite

## Slide 6: Simulation and Design Capabilities
CST Suite: 3D structure simulator (filters, circulators, …)
Microwave Office: Harmonic Balance Analysis (mixers, multipliers)

## Slide 7: Amplifier bonding (clean room, space standards)
Mounting of all amplifier types
Experience in micromachining
Bonding and soldering to space standards

## Slide 8: Schottky Mixer and Multiplier Improvements
Planar technology
Discrete Schottky devices
Semi-integrated and full integrated structures
Two collaborations:
STFC/RAL, UK
ACST, Germany
Mandatory improvements
for 800 to 1000 GHz
circuit mountings:
Reduced Cj0
Reduced Cstr
Smaller size
ESTEC Contract 22032/08/NL/JA: Sub-Millimeter Wave Receiver Front-End (at 664 GHz)
ESTEC Contract 21628/08/NL/GLC: Integrated Schottky Structures (at 664 GHz)
Air-bridge
Mesa with
anode
Anode pillar
(contact pad)
Cathode pillar
(contact pad)
Back-side ohmic
Membrane-
substrate
Air-bridges
Mesas
Protection pillars
(contact pads)
Back-side ohmic
Membrane-
substrate
25μm
50μm
Quasi-vertical (QVD) single Diode (SD)
Anti-parallel (APD) diode
RAL Diode
ACST Diode

## Slide 9: Sample pictures
Integrated SHM 664 GHz
RAL APD
UMS
ACST
Diode
UMS MMIC 50-100 GHz
900GHz Substrate
ACST/RAL 300-664 GHz

## Slide 10: Improved Schottky Diodes: VNA Extender
OEM
Network Analyzer Frequency Extenders
for
Rohde & Schwarz
50 – 75 GHz
60 – 90 GHz
75 – 110 GHz
90 – 140 GHz
110 – 170 GHz
140 – 220 GHz
220 – 325 GHz 325 – 500 GHz
(500 – 750 GHz)
Courtesy of Rohde & Schwarz

## Slide 11: Improved Diodes: RPG sub-harmonic mixers
Art.-No. | RF Range [GHz] | DSB-Noise Temperature | Conversion Gain (DSB) | IF-Band- width | Required LO Power | Waveguide LO RF | 
SHM118 | 104-132 | 500 K | -5 dB | > 16GHz | 6 dBm | WR15 | WR8
SHM137 | 110-165 | 500 K | -6 dB | > 20 GHz | 4-7 dBm | WR12 | WR6.5
SHM150 | 134-167 | 450 K | -6 dB | > 16 GHz | 2 dBm | WR12 | WR6.5
SHM183 | 167-200 | 430 K | -4 / -5 dB | > 16 GHz | 4 dBm | WR10 | WR5.1
SHM220 | 185-230 | 500 K | -6 dB | > 18 GHz | 4-7 dBm | WR10 | WR5.1
SHM280 | 265-295 | 700 K | -7 dB | > 18 GHz | 4-7 dBm | WR6.5 | WR3.4
SHM300 | 275-330 | 900 K | -7 dB | > 18 GHz | 4-7 dBm | WR6.5 | WR3.4
SHM340 | 310-360 | 1000 K | -6 / -7 dB | > 16 GHz | 4-7 dBm | WR6.5 | WR2.8
SHM424 | 400-440 | 1100 K | -7/ -8 dB | > 16 GHz | 7 dBm | WR4.3 | WR2.2
SHM664 | 644-680 | 1600 K | -8 dB | > 16 GHz | 4-7 dBm | WR3.4 | WR1.5

## Slide 12: Receiver technology – 183 GHz example
Best 183 GHz receivers available
Built in larger numbers
Noise-injection calibration @183 (RPG only manufacturer world wide)
All ALMA water vapor radiometers equipped with RPG mixers and feeds
183 GHz feeds and sub-harmonic
mixers for ALMA-WVR

## Slide 13: Space Products

## Slide 14: Space Products (II)
Space qualified front ends (China, FY-3):
90 GHz dual polarized receiver OMT + LNA + (either Direct Detection or Heterodyne)
150 GHz dual polarized receiver: OMT + SHM

## Slide 15: Preparations for MetOp-SG Ice Cloud Imager

## Slide 16: Space Products (III)
Space qualified front ends:
183 GHz (4 channels) for sensitive water vapour detection
90 GHz dual polarized receiver
150 GHz dual polarized receiver

## Slide 17: Auto-Calibration Receivers
17
Allan Variance Stability: 4.000 s
Less dependent on external calibration
targets (LN2)!
Noise injection calibration up to 200 GHz
  7.000 K signal at 183 GHz with stable noise diode (15 dB ENR)
Magnetically switched isolators: Dicke switching up to 150 GHz with low insertion loss (≤1.0 dB)
  Fast switching with low currents (small thermal effects, 100 mA, 0.5 V)
ESA-ATPROP 15 / 90 GHz

## Slide 18: Sub-mm imaging receivers
One-Pixel and Multipixel Receiver:
FMCW Radar 75 to 325 GHz
CW Radar
8-Pixel Array 230-320 GHz (ESA) and 8-Pixel Array 812 GHz,
4-Pixel Array 183 GHz
Imaging, Security, Material Analysis, Science

## Slide 19: Antenna Measurement Solutions
Transmit / Receive Systems, Spectrum Analyzer Solutions:
Full-band 50-75 GHz 60-90 GHz 75-110 GHz 110-170 GHz 140-220 GHz 170-260 GHz 220-325 GHz 260-400 GHz 325-500 GHz
High Dynamic Receivers available at 90 GHz 183 GHz 220 GHz 324 GHz 502 GHz 640 GHz
For compact ranges (antenna measurement facilities, phase + amplitude)

## Slide 20: Radiometer Products
Approx. 25 standalone multi-channel radiometers per year

## Slide 21: Radiometers Deployments
Lampedusa, Italy (humid, hot, salty)
Dome-C, Antarctica
(3.300m, -25 to -80 °C)
Research Vessel “Polarstern” (Atlantic Ocean)
ALMA site, Chile (5.500m above sea level)
Zugspitze, Germany
(2.800m, -35 °C, 250km/h wind)
AMMA campaign, Benin (West-Africa, hot climate, dust)

## Slide 22: Radiometers Deployments
CAOS, Bangalore, India
Zugspitze, Germany, 2650 m asl
Eureka, Ellesmere Island, Canada
Ny-Alesund, Spitsbergen, Norway
Kolkata, India
Solar-Patroller (SST)

## Slide 23: MWSC: Scintillomter @160 GHz for Latent Heat Flux

## Slide 24: MWSC Integration

## Slide 25
RPG-FMCW-94
RPG-FMCW-94-DP
A Cloud Radar by RPG
  Frequency Modulated, Continuous Wave, 94 GHz
  Low mode for fog, high mode up to 12 km
  Re-using RPG technology from Tx/Rx systems and network analysis
  Re-using instrument infrastructure (housing, steering, control, data processing) from microwave radiometers
  Supported by Fraunhofer Institute for RF Technology and Radar (FhG-FHR, Wachtberg, Germany, formerly FGAN)
  Availability: Mid of 2013

## Slide 26: RPG-FMCW-94 Specifications (I)
Operating Frequency: 94 GHz +/-150 MHz
IF Range: 0.5 MHz to 1.3 MHz
Continuous Power: 500 mW (Solid State)
T/R Type: Bi-static
Antenna Diameter: 500 mm
Gain: 52 dB
Chirp Rate: 100 / sec
Chirp Variations: 7
Passive LWP Channel: 89 Ghz (optional)
Dynamic Range: -100 dBz to +20 dBz

## Slide 27: RPG-FMCW-94 Specifications (II)
Ranging: 10 m to 12 km
Sampling Rate: 1 / 4 seconds
Vertical Resolution: 1 m (r: 10m - 600 m)
2 m (r: 0.6 – 1.0 km)
4 m (r: 1.0 – 2.5 km)
8 m (r: 2.5 – 5.0 km)
16 m (r: 5.0 – 12.0 km)
Doppler Resolution: +/- 15 cm/sec
Polarisation: v / h (optional)
  Availability: Mid of 2013
  Possible extensions by
  Additional frequencies
  Passive microwave channels
  Polarisation options

## Slide 28: Reference Customers (selected)
ESA-ESTEC
NASA/JPL
EADS-Astrium
Thales-Alenia Space
SRON (Netherlands)
CNES (France)
DLR (Gerrmany)
Chinese Space Agency (CAS, CSSAR, …)
IRAM
NIST (National Institute for Standards, USA)
PTB (German institute for standards)
CNRS (France)
ESO (European Southern Observatory)
Rohde & Schwarz
AB-millimetre
Aerospace Corporation (USA)
US Air Force, AFRL Research Labs
ROKAF (South-Korean Air Force)
ARM (Atmospheric Radiation Monitoring, USA)
KMA (Korean weather service)
CNRS (France)
UK Met Office
KNMI (The Netherlands weather service)
Meteo Swiss (Switzerland)
Polish weather service
Numerous Universities world wide
AWI Alfred Wegener Institute f. Polar Research
Numerous Universities and Research Institutions